## Slide 1: Kalman Filter on Embedded System
By Devin Renshaw

## Slide 2: Outline
From simulation to system
Complications
Results

## Slide 3: Progression
Using libraries
Simulation
Quick board setup
Fully implemented
Type | Ease | Utility
MATLAB libs | 5 | 2
MATLAB custom | 4 | 2
Arduino | 4 | 4
STM32F0 | 2 | 5

## Slide 4: Arduino/STM implementation
Real-world effects
Sensor noise
Unexpected issues
Port code
Sensors
Compensation

## Slide 5: Issues on Physical Devices
Non-zero mean noise
Temperature effects
Sensor bias/calibration
Sensor drift and jitter
Gimbal lock

## Slide 6: Minor issues
Non-zero mean noise
  Simple shift
Temperature effects
  Wait for stabilization

## Slide 7: Major issues
Sensor bias
  Calibration techniques
Sensor drift and jitter
  Multiple solutions

## Slide 8: Sensor noise and drift
Jitter/noisy
  Estimation technique
    Kalman filters
    Complementary filters (low pass)
Sensor drift
  Compensation (high-pass)

## Slide 9: Sensor drift
What sensors drift?
  Gyroscopes
    Low noise, tend to drift
    Can be deg/min or deg/s
    Drift due to integration
    Hard to mitigate internally
Solutions
  Complementary sensors

## Slide 10: Complementary sensors
Different sensors used
  Accelerometers
  Magnetometers

## Slide 11: Complementary sensors
Accelerometers
  Drift compensation in roll/pitch
  No sensing for yaw
Magnetometers
  Yaw compensation

## Slide 12: Accelerometers
  Compensate for pitch/roll drift
  No sensing for yaw
  Linear acceleration
  Noisy, but no drift

## Slide 13: Magnetometers
  Senses nearby magnetic fields
  Immune to drift
  Susceptible to soft/hard Fe effects

## Slide 14: Hard/Soft Iron Effects
Hard Iron
  Magnetic sources
Soft iron
  Non-magnetized but conductive metals
These effects can be larger than Earth’s magnetic field which we want to measure

## Slide 15
RESULTS

## Slide 16: Timing Comparisons
Complementary vs. Kalman filter
 | Timing (μs) | 
Implementation | Complementary | Kalman
MATLAB | -- | --
Arduino | 120-150 | 2300-2500
STM32F0 | 100-120 | 2200-2300

## Slide 17: Floating point operations
Computationally expensive
Necessary in Kalman filtering
  Fixed point arithmetic didn’t cut it
No HW support for floating point in Arduino or STM32F0
Must be emulated using SW libraries

## Slide 18: Floating Point Operations Cost
Complementary Filter
For both X and Y, only a handful of additions and multiplications are necessary
Relatively inexpensive
Kalman Filter
Matrix operations and many multiplications and additions are necessary
Expensive operations

## Slide 19: Performance
Complementary Filter
Always underperformed Kalman filter
Often took several seconds to settle
Manual setting of α parameter
Not as accurate as Kalman
Kalman Filter
Great results
At most, took fractions of a second to converge
Automatic setting of parameters for estimation
Always returned to within 1⁰ of original position

## Slide 20: Final Results
Kalman filter is great, but expensive
Low-end/power applications may benefit more from complementary filter
Characterizing physical interactions takes a long time